## Slide 1
Lobachevsky State University of Nizhni Novgorod
Computing Mathematics and Cybernetics faculty
The competitiveness enhancement program of the Lobachevsky State University of Nizhni Novgorod among the world's research and education centers
Strategic initiative “Achieving leading positions in the field of supercomputer technology and high-performance computing”
Supported by Intel

## Slide 2: 01 Lecture Intel Xeon Phi Architecture
Programming for Intel Xeon Phi
I.B. Meyerov, S.I. Bastrakov,
Software department

## Slide 3: Contents
Introduction
Intel Xeon Phi architecture
Core pipeline
Memory hierarchy
Summary

## Slide 4: Introduction

## Slide 5
Image courtesy of Gennady Fedorov, Intel
Notes: Приведенная таблица иллюстрирует направление развития архитектур Intel, соответствующе общей тенденции наращивания производительности за счет использования нескольких уровней параллельности в ЦП – на уровнях использования векторных операций и многих ядер.
Количество ядер сопроцессора Intel Xeon Phi требует уделить особое внимания используемой архитектуре памяти и говорит о том, что работа с памятью неизбежно будет узким местом в приложениях, а использование собственной системы векторных операций - о предпочтительности использования возможностей компилятора для векторизации перед использованием intrinsic.

## Slide 6: Intel Xeon Phi Coprocessor
In 2012 Intel introduces the first device based on Intel MIC (Intel® Many Integrated Core Architecture)
The base of MIC architecture is usage of many x86 cores in one processor
There is a support for standard parallel programming technologies: pthreads, OpenMP, Intel TBB, Intel Cilk Plus, MPI
Intel® Xeon Phi™ 5110P connects to PCIe x16 slot, up to 8 coprocessors on a dual-CPU system

## Slide 7: Intel Xeon Phi Coprocessor
Image source: http://www.intel.com/content/www/us/en/processors/xeon/xeon-phi-coprocessor-datasheet.html

## Slide 8: Intel Xeon Phi architecture

## Slide 9: Intel Xeon Phi architecture
61 cores
High performance ring bus
8 memory controllers support 16 GDDR5 channels
A separate component implements client PCI Express logic
Image source: https://software.intel.com/en-us/articles/intel-xeon-phi-coprocessor-codename-knights-corner (Figure 3)

## Slide 10: Intel Xeon Phi core…
Performs fetching and decoding of instructions of 4 hardware threads
Supports 32- and 64-bit code compatible with Intel64 architecture
Each core contains 2 pipelines: (U-pipe and V-pipe) and is capable of executing 2 instructions per cycle
  V-pipe is not capable of executing all types of instructions, a possibility of parallel execution on U- and V-pipes is defined by a set of rules
Image source: https://software.intel.com/sites/default/files/article/335818/intel-xeon-phi-coprocessor-quick-start-developers-guide.pdf (Fig 2)

## Slide 11: Intel Xeon Phi core
Out-of-order execution is not supported
No support to instruction sets Intel Streaming SIMD Extensions (SSE), MMX and Advanced Vector Extensions (AVX)
32 Kb of 8-channel multi-associative instruction and data caches (L1 I-Cache и L1 D-Cache)
Image source: https://software.intel.com/sites/default/files/article/335818/intel-xeon-phi-coprocessor-quick-start-developers-guide.pdf (Fig 2)

## Slide 12: Intel Xeon Phi core
512-bit vector processor unit (VPU)
  32 512-bit registers (zmm0-zmm31)
  Extended math unit (EMU)
  On each cycle executes 16 operations with single precision floating point numbers or 32-bit integer numbers or 8 operations with double precision floating point numbers
  Fused multiply-add (FMA) - 32 operations with single precision floating point numbers
  Support for fill-in and permute operations
  8 mask registers for conditional operations
  Supports operations 2x, log2x, 1/x, 1/sqrt(x) for single precision floating point numbers
  One of arguments can be read from memory for type cast
Image source: https://software.intel.com/sites/default/files/article/335818/intel-xeon-phi-coprocessor-quick-start-developers-guide.pdf (Fig 2)

## Slide 13: Intel Xeon Phi core
Core-Ring Interface, CRI/L2
  Connects core to high-performance coprocessor interconnect
  512 Kb of 8-way associative L2 cache
Tag Directory (TD) is part of distributed TD
Image source: https://software.intel.com/sites/default/files/article/335818/intel-xeon-phi-coprocessor-quick-start-developers-guide.pdf (Fig 2)

## Slide 14: Components of Intel Xeon Phi
Image source: https://software.intel.com/en-us/articles/intel-xeon-phi-coprocessor-codename-knights-corner (Figure 8)

## Slide 15: Peak performance
Intel Xeon Phi contains 61 cores, one core is devoted for OS
For single precision floating-point numbers
  16 (vector size) * 2 flops(FMA) * 1.1 (GHz) * 60 (cores) = 2112 GFLOPS
For double precision floating-point numbers
  8 (vector size) * 2 flops (FMA) * 1.1 (GHz) * 60 (cores) = 1056 GFLOPS

## Slide 16: Core pipeline

## Slide 17: Core pipeline of Intel Xeon Phi…
Has 7 stages
VPU has internal pipeline and has 6 stages
All stages of the main pipeline except the last one (WB) support speculative execution
Each core can execute instructions of 4 threads
Pre Thread Picker Function (PPF)
Thread Picker Function (PPF)
Decode Prefixes (D0)
Instruction Decode (D1)
Microcode Control (D2)
Execution (E)
Write Back (WB)

## Slide 18: Core pipeline of Intel Xeon Phi…
Image source: https://software.intel.com/en-us/articles/intel-xeon-phi-coprocessor-codename-knights-corner (Figure 4)

## Slide 19: Core pipeline of Intel Xeon Phi…
Implementation of instruction prefetch (PPF and PF stages) places a limitation on thread execution: two sequential ticks can not execute instruction of the same thread
  To fully utilize Xeon Phi it is required to have at least 2 threads per core. In case there is only 1 thread, its instructions will be prefetched with step of 2 ticks
  Prefetch requires 4-5 ticks if hits instruction cache, much more otherwise. It might be required to have 3-4 threads for optimal performance

## Slide 20: Core pipeline of Intel Xeon Phi
Execution stage (E) is implemented as two pipes: U and V
The first instruction always goes to U-pipe, the second instruction is examined for possibility of simultaneous execution with the first one
Scalar integer operations are performed by ALU. Scalar and vector operations with floating-point numbers have additional 6-stage pipeline
Vector instructions are mostly executed at U-pipe
Most integer and mask instructions have latency 1, most vector instructions have latency 4 or more (if use read/write with fill-in or permutation)

## Slide 21: Memory hierarchy

## Slide 22: Memory hierarchy of Intel Xeon Phi…
All cores use shared coprocessor memory
Each core has private L1 and L2 caches
L1 and L2 caches are inclusive
  All data in L1 is also in L2
L1 and L2 caches use pseudo-LRU algorithm

## Slide 23: Memory hierarchy of Intel Xeon Phi…
L1 caches: L1 I-Cache and L1 D-Cache
  size 32 KB
  lane size 64 bytes
  8-way associative

## Slide 24: Page addressing…
MAX
0
VAS
RAM
HDD
Physical frame number N
…
Physical frame number 1
Physical frame number 0
Page table
CR3
Virtual address space is supported via page transformations

## Slide 25: Page addressing…
Page Global Directory
Page
Page
Page
Page
Page
Page
Page
Page
Page
Page
Page
Page
Page
Page
Page
Page
VAS
Virtual address, 64 bits
47...39
63...48
38...30
20...12
29...21
11...0
Register CR3
Page Upper
Directories
+
...
Page Middle
Directories
+
...
Page Tables
+
...
Page
Page
Page
Page
Page
Page
Page
RAM
+

## Slide 26: Page addressing
Supported page sizes: 4KB and 2 MB
Translation look-aside buffer (TLB) has 2 levels, each core has the following caches

## Slide 27: Summary

## Slide 28: Requirements for applications on MIC
Parameters of Xeon Phi architecture allow to distinguish basic features of an application that define its efficiency when porting to Xeon Phi
  Efficient parallelization on CPU
  Massive parallelism
  Vectorization
  Large computational density
  Using MLK routines
  MPI applications

## Slide 29: Obstacles
Low degree of parallelism
Lots of synchronizations
Intensive use of gather/scatter
Using 64-bit indexes, conversions int64 <-> fp
Intensive communication between host and Xeon Phi
Memory limitation to 8 GB for Xeon Phi
Notes: Использование 64-разрядных индексов или конверсия int64 <-> fp – медленная реализация данных операций является особенностью реализации.

## Slide 30: Notes on boosting performance
Problem size
  Large problems have greater degree of parallelism
  But not very large (memory limit 8 GB)
Data alignment
  64 bytes for efficient vectorization
Number of OpenMP threads and affinity
  Avoid thread migration to preserve data locality
Huge memory pages
  Reduces TLB cache miss rate

## Slide 31: References
Reinders J. An Overview of Programming for Intel Xeon processors and Intel Xeon Phi coprocessors.
  [http://software.intel.com/en-us/blogs/2012/11/14/an-overview-of-programming-for-intel-xeon-processors-and-intel-xeon-phi]
Loc Q Nguyen et al. Intel Xeon Phi Coprocessor Developer's Quick Start Guide.
  [http://software.intel.com/en-us/articles/intel-xeon-phi-coprocessor-developers-quick-start-guide]
Intel Xeon Phi Coprocessor System Software Developers Guide
  http://software.intel.com/en-us/articles/intel-xeon-phi-coprocessor-system-software-developers-guide]
Rahman R. Intel Xeon Phi Core Microarchitecture
  [http://software.intel.com/en-us/articles/intel-xeon-phi-core-micro-architecture]

## Slide 32: Authors
I.B. Meyerov, PhD, associate professor, vice-head of the Software department of CMC faculty meerov@vmk.unn.ru
S.I. Bastrakov,
Assistant of Software department, CMC faculty
bastrakov@vmk.unn.ru