## Slide 1
Lobachevsky State University of Nizhni Novgorod
Computing Mathematics and Cybernetics faculty
The competitiveness enhancement program of the Lobachevsky State University of Nizhni Novgorod among the world's research and education centers
Strategic initiative “Achieving leading positions in the field of supercomputer technology and high-performance computing”

## Slide 2: 01 Lecture General purpose computing on GPU
Introduction to GPU programming
Bastrakov S.I.
Software department

## Slide 3: Contents
Why GPU?
Overview of GPU architecture
Overview of GPU programming technologies
Heterogeneous computing on CPUs and GPUs

## Slide 4: Why GPU?

## Slide 5: Heterogeneous computing and GPGPU
Heterogeneous (hybrid) computing is computing using different kinds of computational hardware.
Most popular kinds of hardware:
  CPUs;
  Intel Xeon Phi coprocessors;
  GPUs;
  specialized processors (DSP and others);
  FPGAs.
Most popular heterogeneous combination is currently CPU + GPU.
GPGPU is general-purpose computing on GPU.

## Slide 6: Typical GPGPU applications
Physical simulation
Visual effects
Financial computing
Computational biology and chemistry
Examples:
http://www.nvidia.com/object/cuda_showcase_html.html
http://developer.amd.com/zones/openclzone/pages/openclappexamples.aspx

## Slide 7: Peak performance of CPUs and GPUs
Image source: NVIDIA CUDA C Programming Guide v. 6.5

## Slide 8: Memory bandwidth of CPUs and GPUs
Image source: NVIDIA CUDA C Programming Guide v. 6.5

## Slide 9: Modern GPUs
Modern GPUs are massively parallel processors.
High performance and memory bandwidth.
Fits for many classes of computationally intensive problems.
Advanced programming languages and tools.

## Slide 10: Why not GPU?
Not all problems can be parallelized on large amount of threads.
Not all problems fit GPU architecture.
Code development and optimization is more complicated compared to traditional programming.
Many problems have computationally intensive subproblems that can be efficiently ported to GPU.

## Slide 11: Overview of GPU architecture

## Slide 12: Architecture of CPUs and GPUs
CPU
“cache-oriented”
GPU
“cache-miss oriented”
Image source: NVIDIA CUDA C Programming Guide v. 6.5

## Slide 13: Architecture of CPUs and GPUs
GPU architecture is aimed at computing that is:
  data parallel: each operation is performed for many elements in parallel,
  big computational density.
Compared to СPU:
  much less cache and control logic
  much more computational elements
Memory latency is covered by using large amount of lightweight threads.
CPU architecture is gradually becoming more parallel, GPU architecture is gradually becoming more sophisticated.

## Slide 14: NVIDIA GPU architecture
Consists of streaming multiprocessors (MP), each contains several CUDA-cores and shared memory.
  In first CUDA devices CUDA-cores were called scalar processors (SP).
CUDA-cores of one multiprocessor work as one or several SIMD units.
Extremely lightweight threads, hardware thread scheduler.

## Slide 15: Multiprocessor of NVIDIA Fermi architecture
Image Source: А.В. Боресков, А.А. Харламов «Архитектура и программирование массивно-параллельных вычислительных систем»

## Slide 16: Overview of GPU programming technologies

## Slide 17: Stream computing model
GPUs use stream computing model.
Data stream is a sequence of uniform elements that can be processed independently.
A function that processes one element is called kernel.
Kernel body handles one element, kernel is called many times (maybe in parallel), once per each element.
  Example: sum of two vectors of length N, kernel body adds a pair of numbers, kernel is called N times.
GPU programming technologies use stream computing model.

## Slide 18: Shading languages
Historically first tool that could be used for GPGPU (although not designed for it)
Shading languages are used to write pieces of code that is executed on GPU hardware, so-called shading processors
All programming is done in graphics terms
One of the most popular shading languages is GLSL (OpenGL Shading Language)

## Slide 19: Metaprogramming tools BrookGPU и Sh
Metaprogramming: a program is written in a high-level language that is later automatically translated to shading languages.
Much more simple to use compared to shading languages.
A tradeoff is efficiency, the code is hard to optimize for a specific hardware.
Now these tools are not supported, by they have given birth to other technologies:
  Sh became RapidMind that was consumed by Intel in 2009.
  Improved version of BrookGPU was part of AMD Stream as Brook+.

## Slide 20: NVIDIA CUDA and AMD Stream
NVIDIA CUDA: February 2007.
AMD Stream Computing: November 2007.
Have similar structure:
  Low level: GPU assembly, memory management.
  High level: stream extensions of C language, high performance libraries, profiling and debugging tools.
Advantages:
  Programming in extensions of C language.
  Access to hardware features and low-level optimization.
Disadvantages:
  Programming requires some knowledge of architecture.
  Porting is not easy.

## Slide 21: OpenCL
OpenCL – Open Computing Language.
Open standard for heterogeneous computing developed by Khronos Group in collaboration with vendors.
First version: November 2008.
Supported by Apple, NVIDIA, AMD, Intel, IBM, and others.
Supports a wide range of hardware due to programming in terms of abstract models of hardware.
Applications are portable. Performance is not always high, but usually reasonable

## Slide 22: OpenACC
Standard for heterogeneous computing on multicore CPUs and GPUs.
Concept is similar to OpenMP (and particularly #pragma offload for Xeon Phi)
Limited access to low-level optimization and memory management
Ideally suited for quick porting of large applications
Performance-critical parts might be later implemented and optimized using CUDA

## Slide 23: Heterogeneous computing on CPUs and GPUs

## Slide 24: Motivation
Heterogeneous systems are becoming more and more popular:
  APU (accelerated processing unit) combine CPU and GPU cores.
  Intel Xeon Phi (MIC, many integrated cores) coprocessors contain about 60 cores.

## Slide 25: Motivation
Most popular heterogeneous combination is currently CPU + GPU.
Peak performance of modern GPUs is largely superior over CPUs.
However, a gap is usually smaller on real applications.
It makes sense to use both CPUs and GPUs simultaneously

## Slide 26: Motivation
In applications using CUDA or OpenCL host part is usually playing only utility role:
  Initialization.
  Running kernels.
  Data exchanges.
It does not place a great computational load on CPU and does not require all CPU cores.
Thus, some (or all) CPU cores can be used for computing.

## Slide 27: Load balancing
Load balancing is required because of different nature of hardware being used:
  Performance
  Data transfers: CPU cores use shared memory, need data transfers between CPU and GPU or GPU and another GPU.
Inefficient load balancing can cause data transfer overheads to ruin performance gains.

## Slide 28: Summary
GPUs are massively parallel processors that are well suited for data parallel applications
GPU programming technologies mainly use stream computing model
Most popular technologies are CUDA, OpenCL, OpenACC
Heterogeneous computing becomes more popular
Load balancing needs to be address thoroughly

## Slide 29: Summary
Appropriate algorithms that allow high degree of parallelism need to be chosen for implementation on GPU
Typical scheme of problem decomposition is:
  decomposition into large amount (thousands or more) of sub-problems that can be solved independently;
  decomposition into small amount of sub-problems that can be solved independently, decomposition of each sub-problem into hundreds of smaller problems.
High computational density is preferable.
Usually CPUs are used for sequential parts of an application and GPUs are used for massively parallel part.

## Slide 30: References
Sanders J., Kandrot E. CUDA by Example: An Introduction to General-Purpose GPU Programming. – Addison-Wesley Professional, 2010. – 312 p.
NVIDIA CUDA C Programming Guide. [http://docs.nvidia.com/cuda/cuda-c-programming-guide/].

## Slide 31: Authors
Bastrakov S.I., Assistant of the Software department of CMC faculty. bastrakov@vmk.unn.ru