## Slide 1
Lobachevsky State University of Nizhni Novgorod
Computing Mathematics and Cybernetics faculty
The competitiveness enhancement program of the Lobachevsky State University of Nizhni Novgorod among the world's research and education centers
Strategic initiative “Achieving leading positions in the field of supercomputer technology and high-performance computing”

## Slide 2: 05 Lecture CUDA thread execution and memory hierarchy
Introduction to GPU programming
Bastrakov S.I.
Software department

## Slide 3: Contents
GPU architecture
Thread execution
Memory hierarchy

## Slide 4: GPU architecture

## Slide 5: CPU and GPU architecture
CPU
“cache-oriented”
GPU
“cache-miss oriented”
Image source: NVIDIA CUDA C Programming Guide v. 6.5

## Slide 6: Tesla 8 multiprocessor
Image source:A.V. Boreskov, A.A. Harlamov “Architecture and programming of massively parallel computational systems”.

## Slide 7: Tesla 10 multiprocessor
Image source:A.V. Boreskov, A.A. Harlamov “Architecture and programming of massively parallel computational systems”.

## Slide 8: Tesla 10 memory hierarchy
device/global
shared
constant cache
texture cache
register
local

## Slide 9: Fermi multiprocessor
Image source:A.V. Boreskov, A.A. Harlamov “Architecture and programming of massively parallel computational systems”.

## Slide 10: Thread execution

## Slide 11: Thread communication
Threads of the same block are executed on the same multiprocessor, they can communicate using:
  shared memory;
  __syncthreads().
Threads of different block can communicate only via global memory.
There are atomic operations in shared and global memory.

## Slide 12: Kernel execution
Blocks are distributed between multiprocessors
Threads of a block are executed by CUDA-cores of a multiprocessor
If there are enough resources, several blocks can be concurrently executed on the same multiprocessor.
Large amount of blocks helps automatic scaling.

## Slide 13: Automatic scaling
Image source: NVIDIA CUDA C Programming Guide v. 6.5

## Slide 14: SIMT
All threads running on the same multiprocessor are grouped in warps, a warp consists of threads with sequential identifiers.
  Warp size is currently 32.
Warp scheduling is done automatically.
CUDA-cores of a multiprocessor execute same instruction for all threads in a warp (SIMT, Single Instruction Multiple Thread).
  Threads of a warp are always synchronized.
Programming in scalar terms: kernel code for one thread, can use conditions.

## Slide 15: Example of warp execution
Image source: NVIDIA CUDA C Programming Guide v. 6.5

## Slide 16: Memory hierarchy

## Slide 17: Memory hierarchy
*+ L1/L2 cache from Fermi
Memory type | Access | Scope | Speed
Register | R/W | Per-thread | High (on-chip)
Local | R/W | Per-thread | Low (DRAM)
Shared | R/W | Per-block | High (on-chip)
Global* | R/W | Per-grid | High if hit cache (DRAM)
Constant | R/O | Per-grid | High if hit cache
Texture | R/O | Per-grid | High if hit cache
Image source:A.V. Boreskov, A.A. Harlamov “Architecture and programming of massively parallel computational systems”.

## Slide 18: Using global memory
cudaError_t cudaMalloc (void** devPtr, size_t count
cudaError_t cudaFree (void* devPtr)
cudaError_t cudaMemcpy (void* dst, const void* src, size_t count, enum cudaMemcpyKind kind),
  kind can be cudaMemcpyHostToDevice and cudaMemcpyDeviceToHost.
cudaMemcpyAsync – asynchronous version.

## Slide 19: Example
Allocate arrays on host and device:
int n = 1000;
float * a = new float[n], * a_gpu;
cudaMalloc((void**)&a_gpu, n * sizeof(float));
Copy from host to device:
cudaMemcpy(a_gpu, a, n * sizeof(float),
cudaMemcpyHostToDevice);
Copy from device to host:
cudaMemcpy(a, a_gpu, n * sizeof(float),
cudaMemcpyDeviceToHost);

## Slide 20: Coalescing for global memory…
Image source: NVIDIA CUDA C Programming Guide v. 6.5

## Slide 21: Coalescing for global memory…

## Slide 22: Coalescing for global memory
Image source: NVIDIA CUDA C Programming Guide v. 6.5

## Slide 23: Example: Jacobi method
__global__ void kernel (float * a, float * f, float * x0, float * x1, int n)
{
int idx = blockIdx.x * blockDim.x + threadIdx.x;
int ia = n * idx;
float sum = 0.0f;
for (int i = 0; i < n; i++)
sum += a[ia + i] * x0[i]; /* no coalescing! */
float alpha = 1.0f / a[ia + idx];
x1[idx] = x0[idx] + alpha * (f[idx] - sum);
}

## Slide 24: Working with shared memory
Latency 4 clocks.
Small size (16 to 48 KB).
Typical use pattern:
  Load intensively used data from global memory;
  Synchronize if necessary;
  Compute using loaded data;
  Synchronize if necessary;
  Write results back to global memory.

## Slide 25: Example
__global__ void kernel(int * a)
{
int globalIdx = blockIdx.x * blockDim.x + threadIdx.x;
__shared__ int shared_a[NUM_THREADS];
shared_a[threadIdx.x] = a[globalIdx];
__syncthreads();
// all threads of a block can use shared_a
}

## Slide 26: Dynamically allocated shared memory
array0 of type short length 2n, array1 of type float length n and array2 of type int length 3n.
extern __shared__ float array[];
__global__ void kernel(int n) {
short* array0 = (short*)array;
float* array1 = (float*)&array0[2 * n];
int* array2 = (int*)&array1[n];
}
…
int shared_mem_size = sizeof(short) * 2 * n + sizeof(float) * n + sizeof(int) * 3 * n;
kernel<<<num_blocks, num_threads, shared_mem_size>>>(n);

## Slide 27: No bank conflicts
Image source: NVIDIA CUDA C Programming Guide v. 6.5

## Slide 28: Bank conflicts
Image source: NVIDIA CUDA C Programming Guide v. 6.5

## Slide 29: References
Sanders J., Kandrot E. CUDA by Example: An Introduction to General-Purpose GPU Programming. – Addison-Wesley Professional, 2010. – 312 p.
Farber R. CUDA Application Design and Development. – Morgan Kaufmann, 2011. – 336 p.
NVIDIA CUDA C Programming Guide. [http://docs.nvidia.com/cuda/cuda-c-programming-guide/].

## Slide 30: Authors
Bastrakov S.I., Assistant of the Software department of CMC faculty. bastrakov@vmk.unn.ru